December 31, 2013

GPA13-00002 Mission Academy Residential Community

Engineering comments (2nd.  Submittal)

- (Repeat comment) - Please show the designated A-99 flood zone area(s) on this project.  Use the A-99 base flood elevation to design for areas that are in this flood zone.

- (Repeat comment) - There are eight existing parcels for this GPA.  Please clarify how these parcels will be converted to the proposed six lots, per Map Act.

- (Repeat comment) - Please refer to the typical street sections.  The typical street sections should comply with the Engineers Design Standards, and should be consistent with the Mission San Luis Rey Historic Area (Res. No. 86-H11) design criteria.

- (Repeat comment) - Please show the lane assignment on Academy Road at the intersection with Mission Avenue.

- (Repeat comment) - Please show the left turn pocket on Mission Avenue at the intersection with Academy Road based on the 3640 ADT peak hour factor.

- (Repeat comment) - Please show the estimated grading quantities for each proposed lots (each of the six lots).  What area is the grading quantity shown on the conceptual plan?

- Place a statement on the conceptual plan:  There shall be no direct drainage discharge, and there shall be no grading on top of the existing 20 feet Storm Drain & Sewer easement along the eastern boundary of lot number two.

- Please address the drainage impact on downstream system (there is a history of flooding in the mobile home park).

- Please respond to Storm Water Management Plan (SWMP) comments.