Oceanside Building Division

Community Development Department

TO:	Project Planning

FROM:	Building Division

DATE:	Dec. 20, 2013

SUBJECT:	SFD

GPA13-00002

BUILDING DIVISION CONDITIONS:

1)          The granting of approval under this action shall in no way relieve the applicant/project from compliance with all Current State and local building codes. Applicable Building Codes and Ordinances shall be based on the date of submittal for Building Division plan check. Jan. 1, 2014 the State of California will be under the 2013 CBC based on the 2011 IBC.

2)      The building plans for this project shall be prepared by a licensed architect or engineer and shall be in compliance with this requirement prior to submittal for building plan review.

3)          All outdoor lighting shall meet Chapter 39 of the City Code (Light Pollution Ordinance) and shall be shielded appropriately. Where color rendition is important high-pressure sodium, metal halide or other such lights may be utilized and shall be shown on final building and electrical plans.

4)        All electrical, communication, CATV, etc. service lines within the exterior lines of the property shall be underground  (City Code Sec. 6.30).

5)         Compliance with the Federal Clean Water Act (BMP’s) shall be demonstrated on the plans.  Separate/unique addresses may be required to facilitate utility releases.  Verification that the addresses have been properly assigned by the City’s Planning Division shall accompany the Building Permit application.

6) A complete Soils Report, Structural Calculations, & Energy Calculations/documentation shall be required at time of plans submittal to the Building Division for plan check.

7)      A private sewer system design shall be submitted to the Building Division and approved prior to the construction of the sewer system.  If a gravity flow system is not used, an engineered mechanical system shall be submitted and approved by all City of Oceanside Departments.

7)          Site development, parking, Restrooms, access into buildings and building interiors shall comply with Part 2, Title 24, C.C.R. (Disabled Access –Nonresidential buildings - D.S.A.).

9)          The developer shall monitor, supervise and control all building construction and supportive activities so as to prevent these activities from causing a public nuisance, including, but not limited to, strict adherence to the following:

a)      Building construction work hours shall be limited to between 7 a.m. and 6 p.m. Monday through Friday, and on Saturday from 7 a.m. to 6 p.m. for work that is not inherently noise-producing. Examples of work not permitted on Saturday are concrete and grout pours, roof nailing and activities of similar noise-producing nature. No work shall be permitted on Sundays and Federal Holidays (New Year’s Day, Memorial Day, July 4th, Labor Day, Thanksgiving Day, Christmas Day) except as allowed for emergency work under the provisions of the Oceanside City Code Chapter 38 (Noise Ordinance).

b)      The construction site shall be kept reasonably free of construction debris as specified in Section 13.17 of the Oceanside City Code. Storage of debris in approved solid waste containers shall be considered compliance with this requirement. Small Amounts of construction debris may be stored on site in a neat, safe manner for short periods of time pending disposal